## Slide 1
Sewage
Definition: Used water supply of a community/ waste water
Types:
Domestic sewage
Industrial sewage
Storm sewage
Characteristics:
Physical
Chemical
Biological
Composition:

## Slide 3: Physical Characteristics of sewage
1.Temperature:
10 to 21oC with an average of 16oC. In India:15-35oC.
Temperature of wastewater is commonly higher than that of water supply.
2. Colour and Odour:
Fresh waste water - light brownish gray.
With time - dark gray
More time - black (septic)

## Slide 4
Compound Odor quality
Amines Fishy
Ammonia Ammonical
Diamines Rotten eggs
Mercaptans Decayed cabbage
Organic sulfides Rotten cabbage
Skatole Fecal matter

## Slide 5
3. Solids:
1.Total Solids (TS): All the matter that remains as residue upon evaporation at 103oC to 105oC.
2. Settleable solids: An approximate measure of the sludge that can be removed by primary sedimentation.
3. Suspended solids (SS) and Filterable solids (FS)

## Slide 6: Chemical Characteristics of sewage
1. Organic matter:
Derived from animals & plants and man activities
Proteins (40-60%),Carbohydrates (25-50%), Fats, Oils, and Grease (10%).
2. Inorganic matter:
Nitrogen and Phosphorus: N- proteins, amines, amino acids, and urea; P- Phosphates
Chlorides

## Slide 7
3. pH:
Raw sewage 5.5 to 8.0
needs to remain between 6 and 9
4.Gases:
Main gases of concern in wastewater treatment:N2, O2, CO2, H2S, NH3, CH4

## Slide 8: Biological Characteristics
Bacteria, Fungi, Algae, Protozoa, Viruses
Some important bacteria:
Salmonella sp., Vibrio cholerae, Pseudomonas sp., Acinetobacter sp., Nitrosomonas sp., Nitrobacter sp., Coliform bacteria (members of Enterobacteriaceae), Fecal Streptococci, Micrococcus sp., etc.
Fungi: Saprolegnia, Leptomitus, etc.
Algae: Sphaerotilus, Crenothrix, Beggiotoa, Rhodospirillales, etc.
Protozoa: Entamoeba histolytica, Giradia, etc.
Viruses: Enterovirus, Adenovirus, Hepatitis A, etc.

## Slide 9: Waste Water Treatment
Biochemical Oxygen Demand (BOD):
The BOD of the sewage is the amount of oxygen required for the biochemical decomposition of biodegradable organic matter under aerobic conditions.
Oxygen Consumed ~ Decomposable Organic matter
Raw sewage: 100 to 400 mg/L
Expected : less than 30 mg/L

## Slide 10
BOD5: 5 days at 200C
BOD3 : 3 days at 270C
Uses of BOD:
Determination of approximate quantity of oxygen required to react with organic matter
the sizing of the wastewater treatment works
to measure the efficiency of some treatment processes.

## Slide 11: Formula for calculation of BOD
BOD is calculated as:
BOD (mg/l) = (D1 - D2) / P
where D1 = initial DO (mg/l), D2 = final DO (mg/l), and P = fraction of wastewater per total volume of dilution water and wastewater.

## Slide 12: Chemical Oxygen Demand (COD):
The COD gives the measure of the oxygen required for chemical oxidation. It does not differentiate between biological oxidisable and non-oxidisable material.
Oxygen Consumed ~ Decomposable + Non decomposable Organic matter
Requires 3 hours
Range of raw sewage: 200- 700 mg/L

## Slide 13
chemical oxidants (potassium dichromate (K2Cr2O7) or potassium permanganate(KMnO4)
+
organic matter of water
Oxidation of organic matter
Excess Oxygen + KI -->I2
Titrated using sodium thiosulphate and COD is estimated

## Slide 14
COD> BOD
Always

## Slide 15: Theoretical Oxygen Demand (ThOD):
If the chemical formula of the organic matter existing in the WW is known the ThOD may be computed as the amount of oxygen needed to oxidize the organic carbon to carbon dioxide and a other end products.
C6H12O6+ 6O2 6CO2+6H2O

## Slide 16: Waste water treatment:
Preliminary Treatment:
The aim of preliminary treatment processes is to remove large and/or heavy debris which would otherwise interfere with subsequent unit processes or damage pumps and other mechanical equipment in the treatment works. Involves:
Screening
Grit Removal

## Slide 17: Waste water treatment

## Slide 18: Primary Treatment: Sedimentation
Septic tank:
Sewage enters the septic tank
Sedimentation from the upper portion permitting a liquid with fewer suspended solids
Sedimented suspended solids are discharged from the tank and subject to degradation by anaerobic bacteria
Effluent from the septic tank is distributed under the soil surface through the disposal field

## Slide 19: Septic Tank

## Slide 20: Imhoff Tank:

## Slide 21: Secondary Treatment:
Primary aim is removal of dissolved/suspended organic matter biologically
Two types:
Fixed film / attached growth’ digestion
Ex: trickling filter, rotary biological contractors, fluidized bed reactors
Dispersed growth digestion
Ex: stabilization ponds, activated sludge, aerated lagoons

## Slide 22: Organic Matter + Bacteria + O2 New Cells (Biomass) + CO2, H2O, NH3

## Slide 23: Process in Fixed film reactor

## Slide 24: 1) Trickling Filters

## Slide 25: Components of TF:
1. A dosing system for applying the wastewater
2. A bed of randomly packed solid media
3. An under drainage system for collection of the treated effluent
4. A ventilation system for supplying oxygen to the filter
5. A system for separating the detached biofilm (also called humus) from the treated effluent.

## Slide 27
biological activity of the biofilm is the primary mechanism of removal of dissolved organic matter
short contact time (20-30 seconds)
microbial community includes a mixture of bacteria, protozoa, and fungi > forms zoogleal film/biofilm (thickness is << 1mm)

## Slide 28: 2 ) Rotating Biological Contactors:

## Slide 30: Dispersed growth digestion:
Stabilization Ponds or oxidation ponds:
The stabilization ponds are classified as:
1. Anaerobic ponds
2. Facultative ponds
3. Maturation ponds

## Slide 31: Anaerobic ponds: Shallowest

## Slide 32: Facultative ponds :

## Slide 33: Maturation ponds

## Slide 34: Activated Sludge System
Aerobic digestion
Anaerobic digestion

## Slide 35: Aerobic sludge digester

## Slide 36: Anaerobic Sludge digester

## Slide 37: Tertiary wastewater treatment:
any physicochemical or biological process employing bioreactors, precipitation, filtration, or chlorination procedures
sharply reduces levels of inorganic nutrients, especially phosphate, nitrite, and nitrate, from the final effluent

## Slide 38: Operations in tertiary treatment
use of activated carbon
Oxidation with ozone
reverse osmosis or distillation